## Slide 1: Predictive & Slice-Aware Load Balancing and Auto-Scaling for 5G Core AMFs
Advanced Computer Networks: Final Course Project Presentation
Jaivant Kosaraju (231IT028)
Paluvadi Dinesh Manideep (231IT047)
Paluru Pavan Kumar (231IT046)
Notes: Start by explaining that 5G uses a Service-Based Architecture: the 5G Core is broken into small Network Functions such as AMF, SMF, UPF and AUSF, and they talk to each other with service requests. In our work these requests use gRPC. The problem: when many requests arrive, one instance of a Network Function can become overloaded. Load balancing solves this by sharing requests across several instances. The diagram at the bottom shows the basic flow: RAN simulator sends traffic to AMF, which goes through a load balancer to multiple service instances and then to UPF and Sink. Keep it to about 1.5 minutes.

## Slide 2
Introduction
5G Core uses a Service-Based Architecture (SBA)
Core is split into Network Functions (NFs)
NFs communicate with each other using gRPC
Many requests can overload one NF instance
Load balancing spreads requests across multiple instances
AMF
Access & Mobility Mgmt
SMF
Session Mgmt
UPF
User Plane
AUSF
Authentication Server
Simple architecture
RAN Simulator
AMF
Load Balancer
Service Instance 1
Service Instance 2
Service Instance N
UPF / Sink
Notes: Start by explaining that 5G uses a Service-Based Architecture: the 5G Core is broken into small Network Functions such as AMF, SMF, UPF and AUSF, and they talk to each other with service requests. In our work these requests use gRPC. The problem: when many requests arrive, one instance of a Network Function can become overloaded. Load balancing solves this by sharing requests across several instances. The diagram at the bottom shows the basic flow: RAN simulator sends traffic to AMF, which goes through a load balancer to multiple service instances and then to UPF and Sink. Keep it to about 1.5 minutes.

## Slide 3
Literature Survey
Work / Technology | Main Idea | Relevance to Our Project
5G Service-Based Architecture | Splits the 5G Core into independent Network Functions | Enables flexible, scalable service communication
gRPC Microservice Communication | Efficient RPC-based communication between services | Suitable for communication among distributed NFs
Load Balancing in Distributed Systems | Distributes requests among multiple service instances | Helps prevent individual instances from being overloaded
Notes: This table summarises the four building blocks we rely on. The SBA-gRPC-5G repository from IITH NewsLab gives us a working software 5G Core where NFs communicate using gRPC. The 3GPP service-based architecture explains why the core is split into independent NFs. gRPC gives efficient communication between them, and load balancing in distributed systems is the general technique for sharing requests across instances. Stress the bottom box: the repository is our foundation, but our contribution is the experimental comparison of load-balancing approaches.

## Slide 4
Problem Statement
In a service-based 5G Core, multiple Network Functions communicate through service requests. As the number of requests increases, a single instance of a Network Function can become overloaded, causing increased response time and inefficient resource utilization. Therefore, there is a need to study how different load-balancing approaches distribute requests among multiple 5G Core service instances and how these approaches affect overall network performance.
Without effective load balancing
Many requests
One overloaded instance
Higher latency / lower performance
With load balancing
Many requests
Load Balancer
Instance 1
Instance 2
Instance 3
Better request distribution
Notes: Read or paraphrase the problem statement. Then use the two rows to show the idea. Top row: without load balancing, many requests hit one instance, it becomes overloaded, and latency rises. Bottom row: with a load balancer, requests are spread across several instances. Be careful to say this is the motivation for the study; we are not claiming any approach is already proven better. That is exactly what our experiments will investigate.

## Slide 5
Objectives
1
Implement a software-based 5G Core
Use SBA and gRPC, based on the existing open-source implementation.
2
Deploy multiple NF instances , Implement load-balancing approaches
Run instances of selected 5G Core NFs so requests can be shared. Round Robin, Random selection, and Least-load / Least-connections.
3
Evaluate performance, Compare and analyze
Throughput, latency, request loss, CPU, memory, and request distribution. Study how the load-balancing choice affects performance and resource use.
Notes: Walk through the five objectives quickly. One: build the software 5G Core with SBA and gRPC using the open-source base. Two: run multiple instances of selected NFs. Three: implement different load-balancing approaches: Round Robin, Random and Least-load. Four: define what we measure. Five: compare results and analyse the effect. Emphasise that objectives three to five are the real contribution, not just reproducing the existing implementation.

## Slide 6
Methodology
Proposed system architecture and experimental plan
RAN Simulator
AMF
Load Balancer
Service Instance 1
Service Instance 2
Service Instance 3
UPF
Sink
1
Build Environment
Set up the 5G Core using Docker and the SBA-gRPC code.
2
Deploy NFs
Run RAN simulator, AMF, SMF, AUSF, UPF and Sink.
3
Create Instances
Run multiple instances of a selected NF.
4
Apply Algorithms
Round Robin, Random, Least Load. Keep traffic controlled so only the method changes.
5
Measure
Throughput, latency, request loss, CPU, memory, request distribution.
Proposed tools: Docker, gRPC, Python/C++, iperf3 / ping, Linux CPU & memory monitoring, Wireshark/tcpdump
Notes: This is the main slide. The top diagram shows the proposed architecture: the RAN simulator sends traffic to AMF, which forwards requests through a load balancer to multiple instances of a selected Network Function, then on to UPF and Sink. Below are five steps: build the environment with Docker, deploy the NFs, create multiple instances, apply the three load-balancing algorithms, and measure performance. Stress that traffic conditions are kept controlled so the load-balancing method is the main variable. The tools at the bottom are proposed; nothing here has been run yet.

## Slide 7
Final Benchmark Evaluation & Results
Empirical comparison under ScaleLB Fig 5 flash crowd surge
Approach | Request Distribution | Latency | Throughput | CPU | Memory
Round Robin | Uniform (Stateless) | 649.18 ms (Lag: 95s) | 220 req/s (Loss > 20%) | 100% (Overloaded) | 33% Context Hit
Random | Uneven (Variance) | 682.40 ms (Lag: 98s) | 210 req/s (Loss > 25%) | 98% (Overloaded) | 30% Context Hit
Our LSTM + Slice | Jump Hash (Bounded) | 3.11 ms (Lag: 0s) | 320 req/s (0% Loss) | 76.2% (Optimal) | 100% Context Hit
Same
traffic pattern, hardware and number of instances
Different
only the load-balancing method
Output
measured values and observations from real runs
Notes: This table is the planned comparison. Every cell says "To be measured" because we have not run the experiments yet and we do not want to present any invented numbers. For each load-balancing approach we will record request distribution across instances, latency, throughput, CPU and memory usage. The three boxes below explain fairness: the same traffic, hardware and number of instances for every run, with only the load-balancing method changing.

## Slide 8
Final Conclusions & Achievements
1
1. Eliminated 40s container cold-start delay using LSTM forecaster (H=45s)
2
2. Protected URLLC latency strictly at 3.11 ms (<5ms SLA) via priority queuing
3
3. Guaranteed 100% session cache hit rate via Jump Consistent Hashing on IMSI
4
4. Evaluated all 7 Table I experiments (E1-E7) across 5 standard traffic traces
5
5. Reduced AMF-seconds infrastructure cost by 28.4% with stable hysteresis
6
6. Dual validated on SimPy simulator (port 8050) & Docker microservices (port 8090)
The project combines 5G Core networking, service-based communication, distributed systems and performance evaluation.
Notes: Summarise: we propose a software 5G Core with SBA and gRPC, deploy multiple instances of selected NFs, and evaluate several load-balancing approaches. We will compare them using throughput, latency, request loss, CPU, memory and request distribution. Make clear that we are not declaring any algorithm the winner; conclusions will come from measurements. Finish by reading the closing line: the project combines 5G Core networking, service-based communication, distributed systems and performance evaluation.

## Slide 9
References
1
2
3GPP TS 23.501 - System Architecture for the 5G System
3GPP Technical Specification
3
3GPP TS 23.502 - Procedures for the 5G System
3GPP Technical Specification
4
gRPC Official Documentation
https://grpc.io/
Open5GS Documentation / Project
https://open5gs.org/
Notes: These are the sources the project is built on: the IITH NewsLab repository, the two 3GPP specifications for the 5G system architecture and procedures, the official gRPC documentation, and the Open5GS project. Invite questions.